## Slide 1: Introduction to fish processing and preservation

## Slide 2: introduction
Fish is an excellent food for mankind and is easily perishable commodity if it is not properly preserved.
To prevent spoilage of fish, some form of preservation is necessary.
Preservation means, keeping the fish, after landing fit for human consumption for a short or long time.
The cost of preservation should, however low to ensure profitable return.
The method should be simple and applicable on commercial scale and climate of the place.

## Slide 3: Contd…
Besides ensuring availability of fish in a condition fresh and fit, also helps:
In maintaining a steady supply of fish in the market throughout the year.
In keeping a control over the hike and fall in prices.

## Slide 4: CAUSES OF SPOILAGE
Fish is spoiled due to three main factors i.e. chemical, microbial & the enzyme action.
Chemical factors involve oxidation; it causes discoloration, change in viscosity
Microbial action involves bacterial decomposition of fish flesh
Enzymatic action by spoilage of tissues by process of autolysis & make the fish susceptible to bacterial action
Spoilage may be due to some other factors i.e. by copepod (red pepper) are present in stomach & causes spoilage within 24hrs. even of iced fish

## Slide 5: Principles of preservation
The most important principles of preservation of fish is clean sanitation.
Following are the principles involved in fish preservation:
Cleaning:
The main objective is to prevent spoilage of fish from contamination and unhygienic conditions.
The landed fish contains numerous microbes.
Poor sanitary condition and careless handling of fish increased speed of spoilage.

## Slide 6: Contd..
Gutting
Fish is cut along mid ventral side and their visceral organs are removed.
By removing viscera, the bacteria in the gastro intestinal tract and the enzymes of visceral organs are removed along with it to prevent bacterial decomposition and enzyme autolysis.
Raising the Temperature:
Heat decomposes autolytic enzymes.
Moist heat under pressure kills all such bacteria and are known to cause fish spoilage. Used for long term preservation.

## Slide 7: Contd…
Lowering the Temperature:
Very effective in delaying the onset and prolongation of the duration of rigor mortis and in slowing down both autolytic enzyme activity and bacterial multiplication.
At normal room temperature 27-30C, autolysis is fairly rapid.
Quick freezing to -40C destroys many strains of bacteria and makes the surviving ones inactive.
It also control rancidity as well.

## Slide 8: Contd…
Dehydration:
Removal of water content enhances greatly the keeping quality of fish.
Presence of moisture is very favorable for bacterial growth and multiplication.
Loss of moisture curbs bacterial activity and even kills them.
The length of storage depends on degree of dehydration achieved.

## Slide 9: Contd…
Use of salt:
Effective for two reasons:
Brings about removal of moisture from fish by osmosis
Enter the tissues and increases salt concentration to saturation point.
The presence of high salt concentration destroys autolytic enzymes and halts bacterial activity.
Many microbes destroyed as salt has a toxic effect upon them.

## Slide 10: Methods of preservation
Chilling with ice:
Lowering of temperature to about 0C is the most effective method of preventing putrefaction and extending the life of the fish.
This is obtained by covering the fish with layers of ice.
Ice is effective for short term preservation.
Chilled fishes have to be stored properly at a constant temperature nearing the freezing point.

## Slide 11: Contd..
Freezing and refrigeration:
Freezing is more effective than chilling.
Achieved either by using a mixture of ice and salt or refrigeration.
The sub-zero temperature keeps the fish frozen throughout.
During air freezing, water of the flesh separate and form ice crystals, thus the quality of fish is inferior.
Frozen fish is dipped in cold water stored at 10F, Freezing in brine is a rapid process and produces better quality of fish which retains its natural appearance.

## Slide 12: Contd…
Freezing causes loss of flavor and damages tissues.
To prevent rancidity the frozen fish is subjected to glazing with water or wrapped in a cover of moisture proof wax paper or cellophane.
Glazing is, dipping the frozen fish in water so that a layer of hard ice is formed.
This layer affords protection against exposure of fish fat to atmospheric oxygen and preventing rancidity.

## Slide 13: Contd..
Deep Freezing:
It has the advantage of preventing preservation for long time.
Deep freezing permits denaturation, retains freshness and flavor of fish.
Requires rapid lowering of temperature to -40C in half an hr to pass crystal formation.
Before freezing, the fishes are washed and heads are removed.
Freeze drying:
Is a modification of deep freezing, completely eliminating all chances of denaturation.

## Slide 14: Contd…
The deep frozen fish at -20C is then dried by direct sublimation of ice to water vapour without any melting into liquid water.
This is achieved by exposing the frozen fish to 140C in a vacuum chamber of freezing chamber.
The dried fish is packed or canned in air conditioned room.
Canning:
Is done in following steps:
Fishes are clean to remove dirt and organisms present on their body.

## Slide 15: Contd…
Fishes are gutted and cut into pieces of suitable size which are dipped in brine to remove blood and give proper degree of firmness.
Pieces are immersed in hot water or exposed to steam to remove adhering material.
The cleaned pieces are filled in cans or jars which are hot and then passed through an exhaust box receiving steam under pressure.
Exhausting expands food, drives out air or gas bubbles and provides an atmosphere of steam in upper vacant part of the container.
Containers are then immediately sealed.

## Slide 16: Contd…
The sealed containers are again subjected to heat treatment to kill micro-organisms left in flesh.
Sun drying:
Simple method of curing fish and is extensively practiced in Asia.
Drying mean removal of moisture contents of the flesh upto 10%, so that bacterial decomposition and autolysis does not occur.
Drying is of two types i. natural and ii. mechanical

## Slide 17: Contd..
Smoking:
Smoking is another ancient technique that is commonly used with curing
Smoking involves cooking fish very slowly over a low wood fire 130C
Antiseptic action of phenolic acid constituents of smoke
Preserve fish by binding or removing water
Good control is necessary over density, temperature, humidity, speed of circulation, pattern and time of contact with fish.
Smoking increases the flavor of the fish flesh and is very popular.
Salting:
One of the oldest method of fish preservation.
Act as preservative and prevent bacterial growth.
Salting can be dry, wet or brine, fishes are kept in alternate layers with the salt. After few days removed and dried in the sun.

## Slide 18: FISH PRODUCTS/PROCESSING
Fish meat: including boning & fish fillets
Fish meal: containing high percentage of protein, calcium & phosphorus and used as feed for poultry & livestock
Fish oil: Body oil (making of fats, varnish, paint, leather and soap), Liver oil ( valuable source of Vitamin A & D and as lubricant)
Fish Leather: especially from sharks & leather carps in making various leather products

## Slide 19: Fish Transportation

## Slide 20: Transportation of freshly killed fish
Dead fishes should be transported at a low temperature to avoid danger of decomposition of their flesh.
The temperature should be between 0-4C and fish should be placed in crushed ice.
This method stops the development of bacteria and enzymatic and oxidative changes.

## Slide 21: Use of chemicals in live fish transport
The sedatives and disinfectants are also used in transporting medium. The sedation of fish brings in practical benefits by the way of:
Decrease the rate of oxygen consumption and reducing the rate of carbon dioxide, ammonia and other toxic wastes.
Controlling the excitability of fish and reducing chances of injury.

## Slide 22: Measures for Safe transportation
The capture and handling of fish should be done when the habitat is the coolest i.e. during early morning.
The fish should be segregated size wise and if possible species wise.
Warm water should be avoided. Receptacles should not be placed in direct sunrays side.
In hot weather the cans or barrels should be kept in contact with the ice blocks.
Cans can be covered with cloth, soaked with water, thus evaporation of this cloth can maintain freshness inside the can.
Frequently change water over a long journey. Water should be changed slowly.

## Slide 23: Contd..
Optimum load density must be decided.
Jerking should be avoided.
Quantity of fish should be vary according to type of transport.

## Slide 24: FISH MARKETING

## Slide 25: FISH MARKETING
Definition: Fish market is a place inside or out side the country where the fishes & fish products of commercial importance are subjected to sale. These fish production & consumption is properly regulated, is known as fish marketing.
Characteristics of Marketing
1. Perishability of the commodity
Seasonal concentration of landing
Quantity produced by each fisherman is to be assembled, sorted & transported
Non-uniformity of landing, quantity, freshness & size
Handling & treatment, icing, freezing, curing & packing
Large no. of intermediaries involves

## Slide 26: IMPORTANT POINTS RELATED TO SUCCESS OF TRADE
Preliminary estimates of fish production
Establish standards of quality control at various levels
Demand of consumers should be assessed
Price rise or fall should be observed
Keep the fish fresh & avoid spoilage
Improving awareness among public about importance of food as fish
Explore the possibilities of fish preservation & export

## Slide 27: TYPES OF FISH MARKETING
Traditional Fish Marketing
Modern Fish Marketing
Methods of Selling of Fish
Direct buyers
Through commission agents
By contract method

## Slide 28: FLOW OF FISH & FISH PRODUCTS
Fisherman--------------Assemblers--------------------Wholesalers
Intermediaries
Auctioneers
Retailers
Consumers
Flow of money
Consumers--------------------------Retailers---------------------------Auctioneers
Wholesalers
Intermediaries
Assemblers
Fisherman
Normal Cost Structure
Producers-Dealers-Retailers
45%-------23%--------32%

## Slide 29: CORE FISH MARKETING SYSTEM
This may be classified in three types:
Intensive Growth
Market Penetration
Market Development
Products development
Integrative Growth
Backward integration
Horizontal Integration
Forward Integration
Diversification of Growth
Concentric Diversification
Horizontal Diversification
Conglomerate Diversification

## Slide 30: Marketing Organization
Agents & retailers are not suitable for fish exportation, storage & purchase. There is an organization of fish market.
Local Assembled Market
Primary Market
Central Market
Future Market
Function of Organization
Competitive situation of market
willing of sale products
Transport whole selling processing drying to provide salting facilities. This society works on common risk, only trained person works in society, trainers suggest the fisherman.
Local co-operative is made for solving money problems. This co-operative provide money to fishermen in low interest.

## Slide 31: Marketing Improvements
Facilities for credit, finance and loan.
Facilities for distribution, transport and marketing.
Facilities for processing and preservation of fishes.
Facilities for equipment (Crafts and gears).
Facilities for making them aware of the socio economics facts for the welfare of the fishermen and their family members. The socioeconomic facts include rights of fishing lease of water, insurance against-risk of life and property, unprecedented poor catches etc.

## Slide 32: Suggestions to improve-the mode of marketing
By supply a good quality of fish.
By maintaining the nutritional value of the fish.
By exporting fish to other countries to get foreign currency.
By supplying fish to the fish agencies so that consumers may get fresh fish.
By organization-Balance between producer and consumer play an important role in the production of fish. To increase fish production, a cooperative organization being formed by Government which is the association of producer.